## Slide 1
Networking Technologies
AICT012-4-2 and Version VE3
Basic Switch and End Device Configuration

## Slide 2: Topic & Structure of The Lesson
Topic Title | Topic Objective
Cisco IOS Access | Explain how to access a Cisco IOS device for configuration purposes.
IOS Navigation | Explain how to navigate Cisco IOS to configure network devices.
The Command Structure | Describe the command structure of Cisco IOS software.
Basic Device Configuration | Configure a Cisco IOS device using CLI.
Save Configurations | Use IOS commands to save the running configuration.
Ports and Addresses | Explain how devices communicate across network media.
Configure IP Addressing | Configure a host device with an IP address.
Verify Connectivity | Verify connectivity between two end devices.

## Slide 3: Learning Outcomes
At the end of this topic, You should be able to:
Explain the purpose of Cisco IOS
Explain how to access a Cisco IOS device for configuration purposes.
Explain how to navigate Cisco IOS to configure network devices.
Configure hostnames on a Cisco IOS device using the CLI.
Use Cisco IOS commands to limit access to device configurations and save the running configuration
Explain how devices communicate across network media.
Configure a host device with an IP address.
Verify connectivity between two end devices

## Slide 4: Key Terms You Must Be Able To Use
If you have mastered this topic, you should be able to use the following terms correctly in your assignments and exams:
startup-configuration
running-configuration
console
telnet
auxiliary
privileged EXEC access
user EXEC access
Interfaces and Ports
PING
IP address
DHCP

## Slide 5: 2.1 Cisco IOS Access
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 1: Explore the Network

## Slide 6: Cisco IOS Access Operating Systems
Shell - The user interface that allows users to request specific tasks from the computer. These requests can be made either through the CLI or GUI interfaces.
Kernel - Communicates between the hardware and software of a computer and manages how hardware resources are used to meet software requirements.
Hardware - The physical part of a computer including underlying electronics.
Notes: 2 – Basic Switch and End Device Configuration
2.1 – Cisco IOS Access
2.1.1 – Operating Systems

## Slide 7: Cisco IOS Access GUI
A GUI allows the user to interact with the system using an environment of graphical icons, menus, and windows.
A GUI is more user-friendly and requires less knowledge of the underlying command structure that controls the system.
Examples of these are: Windows, macOS, Linux KDE, Apple iOS and Android.
GUIs can fail, crash, or simply not operate as specified. For these reasons, network devices are typically accessed through a CLI.
Notes: 2 – Basic Switch and End Device Configuration
2.1 – Cisco IOS Access
2.1.2 – GUI

## Slide 8: Cisco IOS Access Purpose of an OS
PC operating system enables a user to do the following:
  Use a mouse to make selections and run programs
  Enter text and text-based commands
  View output on a monitor
CLI-based network operating system enables a network technician to do the following:
  Use a keyboard to run CLI-based network programs
  Use a keyboard to enter text and text-based commands
  View output on a monitor
Notes: 2 – Basic Switch and End Device Configuration
2.1 – Cisco IOS Access
2.1.3 – Purpose of an OS

## Slide 9: Cisco IOS Access Access Methods
Console – A physical management port used to access a device in order to provide maintenance, such as performing the initial configurations.
Secure Shell (SSH) – Establishes a secure remote CLI connection to a device, through a virtual interface, over a network. (Note: This is the recommended method for remotely connecting to a device.)
Telnet – Establishes an insecure remote CLI connection to a device over the network. (Note: User authentication, passwords and commands are sent over the network in plaintext.)
***Aux???
Notes: 2 – Basic Switch and End Device Configuration
2.1 – Cisco IOS Access
2.1.4 – Access Methods

## Slide 10: Cisco IOS Access Terminal Emulation Programs
Terminal emulation programs are used to connect to a network device by either a console port or by an SSH/Telnet connection.
There are several terminal emulation programs to chose from such as PuTTY, Tera Term and SecureCRT.
Notes: 2 – Basic Switch and End Device Configuration
2.1 – Cisco IOS Access
2.1.5 – Terminal Emulation Programs
2.1.6 – Check Your Understanding - Cisco IOS Access

## Slide 11: Check your understanding – 2.1 Cisco IOS Access
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 12: 2.2 IOS Navigations

## Slide 13: IOS Navigation Primary Command Modes
User EXEC Mode:
  Allows access to only a limited number of basic monitoring commands
  Identified by the CLI prompt that ends with the > symbol
Privileged EXEC Mode:
  Allows access to all commands and features
  Identified by the CLI prompt that ends with the # symbol
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.1 – Primary Command Modes

## Slide 14: Video - IOS CLI Primary Command Modes
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 15: IOS Navigation Configuration Mode and Subconfiguration Modes
Global Configuration Mode:
  Used to access configuration options on the device
Line Configuration Mode:
  Used to configure console, SSH, Telnet or AUX access
Interface Configuration Mode:
  Used to configure a switch port or router interface
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.2 – Configuration Mode and Subconfiguration Modes

## Slide 16: IOS Navigation Navigation Between IOS Modes
Privileged EXEC Mode:
  To move from user EXEC mode to privilege EXEC mode, use the enabled command.
Global Configuration Mode:
  To move in and out of global configuration mode, use the configure terminal command. To return to privilege EXEC mode, use the exit command.
Line Configuration Mode:
  To move in and out of line configuration mode, use the line command followed by the management line type. To return to global configuration mode, use the exit command.
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 17: IOS Navigation Navigation Between IOS Modes (Cont.)
Subconfiguration Modes:
  To move out of any subconfiguration mode to get back to global configuration mode, use the exit command. To return to privilege EXEC mode, use the end command or key combination Ctrl +Z.
  To move directly from one subconfiguration mode to another, type in the desired subconfiguration mode command. In the example, the command prompt changes from (config-line)# to (config-if)#.
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 18: Video - Navigate Between IOS Modes
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 19: Activity in Netacad: Syntax Checker – Navigate between IOS mode
enable
disable
enable
configure terminal
exit
configure terminal
line console 0
exit
line vty 0 15
exit
interface vlan 1
line console 0
end
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 20: Check your understanding – 2.2 IOS Navigation
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 21: 2.3 The Command Structure

## Slide 22: The Command Structure Basic IOS Command Structure
Keyword – This is a specific parameter defined in the operating system (in the figure, ip protocols).
Argument - This is not predefined; it is a value or variable defined by the user (in the figure, 192.168.10.5).
Notes: 2 – Basic Switch and End Device Configuration
2.3 – The Command Structure
2.3.1 – Basic IOS Command Structure

## Slide 23: The Command Structure IOS Command Syntax Check
A command might require one or more arguments. To determine the keywords and arguments required for a command, refer to the command syntax.
  Boldface text indicates commands and keywords that are entered as shown.
  Italic text indicates an argument for which the user provides the value.
Convention | Description
boldface | Boldface text indicates commands and keywords that you enter literally as shown.
italics | Italic text indicates arguments for which you supply values.
[x] | Square brackets indicate an optional element (keyword or argument).
{x} | Braces indicate a required element (keyword or argument).
[x {y ¦ z }] | Braces and vertical lines within square brackets indicate a required choice within an optional element. Spaces are used to clearly delineate parts of the command.
Notes: 2 – Basic Switch and End Device Configuration
2.3 – The Command Structure
2.3.2 – IOS Command Syntax Check

## Slide 24: The Command Structure IOS Command Syntax Check (Cont.)
The command syntax provides the pattern, or format, that must be used when entering a command.
The command is ping and the user-defined argument is the ip-address of the destination device. For example, ping 10.10.10.5.
The command is traceroute and the user-defined argument is the ip-address of the destination device. For example, traceroute 192.168.254.254.
If a command is complex with multiple arguments, you may see it represented like this:
Notes: 2 – Basic Switch and End Device Configuration
2.3 – The Command Structure
2.3.2 – IOS Command Syntax Check

## Slide 25: The Command Structure IOS Help Features
The IOS has two forms of help available: context-sensitive help and command syntax check.
Context-sensitive help enables you to quickly find answers to these questions:
    Which commands are available in each command mode?
    Which commands start with specific characters or group of characters?
    Which arguments and keywords are available to particular commands?
Command syntax check verifies that a valid command was entered by the user.
    If the interpreter cannot understand the command being entered, it will provide feedback describing what is wrong with the command.
Notes: 2 – Basic Switch and End Device Configuration
2.3 – The Command Structure
2.3.3 – IOS Help Features

## Slide 26: Video - Context Sensitive Help and Command Syntax Check
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 27: The Command Structure Hot Keys and Shortcuts
The IOS CLI provides hot keys and shortcuts that make configuring, monitoring, and troubleshooting easier.
Commands and keywords can be shortened to the minimum number of characters that identify a unique selection. For example, the configure command can be shortened to conf because configure is the only command that begins with conf.
Notes: 2 – Basic Switch and End Device Configuration
2.3 – The Command Structure
2.3.5 – Hot Keys and Shortcuts

## Slide 28: The Command Structure Hot Keys and Shortcuts (Cont.)
The table below is a brief list of keystrokes to enhance command line editing:
Keystroke | Description
Tab | Completes a partial command name entry.
Backspace | Erases the character to the left of the cursor.
Left Arrow or Ctrl+B | Moves the cursor one character to the left.
Right Arrow or Ctrl+F | Moves the cursor one character to the right.
Up Arrow or Ctrl+P | Recalls the commands in the history buffer, beginning with the most recent commands.
Notes: 2 – Basic Switch and End Device Configuration
2.3 – The Command Structure
2.3.5 – Hot Keys and Shortcuts

## Slide 29: The Command Structure Hot Keys and Shortcuts (Cont.)
When a command output produces more text than can be displayed in a terminal window, the IOS will display a “--More--” prompt. The table below describes the keystrokes that can be used when this prompt is displayed.
The table below lists commands that can be used to exit out of an operation:
Note: To see more hot keys and shortcuts refer to 2.3.5.
Keystroke | Description
Ctrl-C | When in any configuration mode, ends the configuration mode and returns to privileged EXEC mode.
Ctrl-Z | When in any configuration mode, ends the configuration mode and returns to privileged EXEC mode.
Ctrl-Shift-6 | All-purpose break sequence used to abort DNS lookups, traceroutes, pings, etc.
Keystroke | Description
Enter Key | Displays the next line.
Space Bar | Displays the next screen.
Any other key | Ends the display string, returning to privileged EXEC mode.
Notes: 2 – Basic Switch and End Device Configuration
2.3 – The Command Structure
2.3.5 – Hot Keys and Shortcuts

## Slide 30: Video – Hot Keys and Shortcuts
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 31: 2.4 Basic Device Configurations

## Slide 32: Basic Device Configuration Device Names
The first configuration command on any device should be to give it a unique hostname.
By default, all devices are assigned a factory default name. For example, a Cisco IOS switch is "Switch.”
Guideline for naming devices:
    Start with a letter
    Contain no spaces
    End with a letter or digit
    Use only letters, digits, and dashes
    Be less than 64 characters in length
Note: To return the switch to the default prompt, use the no hostname global config command.
Notes: 2 – Basic Switch and End Device Configuration
2.4 – Basic Device Configuration
2.4.1 – Device Names

## Slide 33: Basic Device Configuration Password Guidelines
The use of weak or easily guessed passwords are a security concern.
All networking devices should limit administrative access by securing privileged EXEC, user EXEC, and remote Telnet access with passwords. In addition, all passwords should be encrypted and legal notifications provided.
Password Guidelines:
    Use passwords that are more than eight characters in length.
    Use a combination of upper and lowercase letters, numbers, special characters, and/or numeric sequences.
    Avoid using the same password for all devices.
    Do not use common words because they are easily guessed.
Note: Most of the labs in this course use simple passwords such as cisco or class. These passwords are considered weak and easily guessable and should be avoided in production environments.
Notes: 2 – Basic Switch and End Device Configuration
2.4 – Basic Device Configuration
2.4.2 – Password Guidelines

## Slide 34: Basic Device Configuration Configure Passwords
Securing user EXEC mode access:
    First enter line console configuration mode using the line console 0 command in global configuration mode.
    Next, specify the user EXEC mode password using the password password command.
    Finally, enable user EXEC access using the login command.
Securing privileged EXEC mode access:
    First enter global configuration mode.
    Next, use the enable secret password command.
Notes: 2 – Basic Switch and End Device Configuration
2.4 – Basic Device Configuration
2.4.3 – Configure Passwords

## Slide 35: Basic Device Configuration Configure Passwords (Cont.)
Securing VTY line access:
    First enter line VTY configuration mode using the line vty 0 15 command in global configuration mode.
    Next, specify the VTY password using the password password command.
    Finally, enable VTY access using the login command.
Note: VTY lines enable remote access using Telnet or SSH to the device. Many Cisco switches support up to 16 VTY lines that are numbered 0 to 15.
Notes: 2 – Basic Switch and End Device Configuration
2.4 – Basic Device Configuration
2.4.3 – Configure Passwords

## Slide 36: Basic Device Configuration Encrypt Passwords
The startup-config and running-config files display most passwords in plaintext.
To encrypt all plaintext passwords, use the service password-encryption global config command.
Use the show running-config command to verify that the passwords on the device are now encrypted.
Notes: 2 – Basic Switch and End Device Configuration
2.4 – Basic Device Configuration
2.4.4 – Encrypt Passwords

## Slide 37: Basic Device Configuration Banner Messages
A banner message is important to warn unauthorized personnel from attempting to access the device.
To create a banner message of the day on a network device, use the banner motd # the message of the day # global config command.
Note: The “#” in the command syntax is called the delimiting character. It is entered before and after the message.
The banner will be displayed on attempts to access the device.
Notes: 2 – Basic Switch and End Device Configuration
2.4 – Basic Device Configuration
2.4.5 – Banner Messages

## Slide 38: Video – Secure Administrative Access to a Switch
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 39: Activity in Netacad: Syntax Checker - Basic Device Configuration
Secure management access to a switch:
Assign a device name.
Secure user EXEC mode access.
Secure privileged EXEC mode access.
Secure VTY access.
Encrypt all plaintext passwords.
Display a login banner.
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 40: Check your understanding – 2.4 Basic Device Configuration
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 41: 2.5 Save Configurations

## Slide 42: Save Configurations Configuration Files
There are two system files that store the device configuration:
    startup-config - This is the saved configuration file that is stored in NVRAM. It contains all the commands that will be used by the device upon startup or reboot. Flash does not lose its contents when the device is powered off.
    running-config - This is stored in Random Access Memory (RAM). It reflects the current configuration. Modifying a running configuration affects the operation of a Cisco device immediately. RAM is volatile memory. It loses all of its content when the device is powered off or restarted.
    To save changes made to the running configuration to the startup configuration file, use the copy running-config startup-config privileged EXEC mode command.
Notes: 2 – Basic Switch and End Device Configuration
2.5 – Save Configurations
2.5.1 – Configuration Files

## Slide 43: Save Configurations Alter the Running Configurations
If changes made to the running config do not have the desired effect and the running-config has not yet been saved, you can restore the device to its previous configuration. To do this you can:
  Remove the changed commands individually.
  Reload the device using the reload command in privilege EXEC mode. Note: This will cause the device to briefly go offline, leading to network downtime.
If the undesired changes were saved to the startup-config, it may be necessary to clear all the configurations using the erase startup-config command in privilege EXEC mode.
  After erasing the startup-config, reload the device to clear the running-config file from RAM.
Notes: 2 – Basic Switch and End Device Configuration
2.5 – Save Configurations
2.5.2 – Alter the Running Configuration

## Slide 44: Video – Alter the Running Configuration
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 45: Save Configurations Capture Configuration to a Text File
Configuration files can also be saved and archived to a text document.
Step 1. Open terminal emulation software, such as PuTTY or Tera Term, that is already connected to a switch.
Step 2. Enable logging in to the terminal software and assign a name and file location to save the log file. The figure displays that All session output will be captured to the file specified (i.e., MySwitchLogs).
Notes: 2 – Basic Switch and End Device Configuration
2.5 – Save Configurations
2.5.4 – Capture Configuration to a Text File

## Slide 46: Save Configurations Capture Configuration to a Text File (Cont.)
Step 3. Execute the show running-config or show startup-config command at the privileged EXEC prompt. Text displayed in the terminal window will be placed into the chosen file.
Step 4. Disable logging in the terminal software. The figure shows how to disable logging by choosing the None session logging option
Note: The text file created can be used as a record of how the device is currently implemented. The file could require editing before being used to restore a saved configuration to a device.
Notes: 2 – Basic Switch and End Device Configuration
2.5 – Save Configurations
2.5.4 – Capture Configuration to a Text File

## Slide 47: 2.6 Ports and Addresses

## Slide 48: Ports and Addresses IP Addresses
The use of IP addresses is the primary means of enabling devices to locate one another and establish end-to-end communication on the internet.
The structure of an IPv4 address is called dotted decimal notation and is represented by four decimal numbers between 0 and 255.
An IPv4 subnet mask is a 32-bit value that differentiates the network portion of the address from the host portion. Coupled with the IPv4 address, the subnet mask determines to which subnet the device is a member.
The default gateway address is the IP address of the router that the host will use to access remote networks, including the internet.
Notes: 2 – Basic Switch and End Device Configuration
2.6 – Ports and Addresses
2.6.1 – IP Addresses

## Slide 49: Ports and Addresses IP Addresses (Cont.)
IPv6 addresses are 128 bits in length and written as a string of hexadecimal values. Every four bits is represented by a single hexadecimal digit; for a total of 32 hexadecimal values. Groups of four hexadecimal digits are separated by a colon “:”.
IPv6 addresses are not case-sensitive and can be written in either lowercase or uppercase.
Note: IP in this course refers to both the IPv4 and IPv6 protocols. IPv6 is the most recent version of IP and is replacing the more common IPv4.
Notes: 2 – Basic Switch and End Device Configuration
2.6 – Ports and Addresses
2.6.1 – IP Addresses

## Slide 50: Ports and Addresses Interfaces and Ports
Network communications depend on end user device interfaces, networking device interfaces, and the cables that connect them.
Types of network media include twisted-pair copper cables, fiber-optic cables, coaxial cables, or wireless.
Different types of network media have different features and benefits. Some of the differences between various types of media include:
      Distance the media can successfully carry a signal
      Environment in which the media is to be installed
      Amount of data and the speed at which it must be transmitted
      Cost of the media and installation
Notes: 2 – Basic Switch and End Device Configuration
2.6 – Ports and Addresses
2.6.2 – Interfaces and Ports
2.6.3 – Check Your Understanding - Ports and Addresses

## Slide 51: Check your understanding – 2.6 Ports and Addresses
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 52: 2.7 Configure IP Addressing

## Slide 53: Configure IP Addressing Manual IP Address Configuration for End Devices
End devices on the network need an IP address in order to communicate with other devices on the network.
IPv4 address information can be entered into end devices manually, or automatically using Dynamic Host Configuration Protocol (DHCP).
  To manually configure an IPv4 address on a Windows PC, open the Control Panel > Network Sharing Center > Change adapter settings and choose the adapter. Next right-click and select Properties to display the Local Area Connection Properties.
  Next, click Properties to open the Internet Protocol Version 4 (TCP/IPv4) Properties window. Then configure the IPv4 address and subnet mask information, and default gateway.
Note: IPv6 addressing and configuration options are similar to IPv4.
Notes: 2 – Basic Switch and End Device Configuration
2.7 – Configure IP Addressing
2.7.1 – Manual IP Address Configuration for End Devices

## Slide 54: Configure IP Addressing Automatic IP Address Configuration for End Devices
DHCP enables automatic IPv4 address configuration for every end device that is DHCP-enabled.
End devices are typically by default using DHCP for automatic IPv4 address configuration.
  To configure DHCP on a Windows PC, open the Control Panel > Network Sharing Center > Change adapter settings and choose the adapter. Next right-click and select Properties to display the Local Area Connection Properties.
  Next, click Properties to open the Internet Protocol Version 4 (TCP/IPv4) Properties window, then select Obtain an IP address automatically and Obtain DNS server address automatically.
Note: IPv6 uses DHCPv6 and SLAAC (Stateless Address Autoconfiguration) for dynamic address allocation.
Notes: 2 – Basic Switch and End Device Configuration
2.7 – Configure IP Addressing
2.7.2 – Automatic IP Address Configuration for End Devices
2.7.3 – Syntax Checker – Verify Windows PC IP Configuration

## Slide 55: Configure IP Addressing Switch Virtual Interface Configuration
To access the switch remotely, an IP address and a subnet mask must be configured on the SVI.
To configure an SVI on a switch:
  Enter the interface vlan 1 command in global configuration mode.
  Next assign an IPv4 address using the ip address ip-address subnet-mask command.
  Finally, enable the virtual interface using the no shutdown command.
Notes: 2 – Basic Switch and End Device Configuration
2.7 – Configure IP Addressing
2.7.4 – Switch Virtual Interface Configuration
2.7.5 – Syntax Checker – Configure a Switch Virtual interface

## Slide 56: Activity in Netacad - Verify Windows PC IP Configuration
Activity in Netacad- Configure a Switch Virtual Interface
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 57: Video – Test the Interface Assignment
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 58: Video – Test End to End Connectivity
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 59: Quick Review Question
Refer to Quiz - Chapter 2 and Lab Activities in Cisco Networking Academy platform

## Slide 60
Explain the features and functions of Cisco IOS Software.
Configure initial settings on a network device using the Cisco IOS software.
Given an IP addressing scheme, configure IP address parameters on end devices to provide end-to-end connectivity in a small to medium-sized business network.
Summary of Main Teaching Points

## Slide 61: Question and Answer Session
Q & A

## Slide 62: What we will cover next
Protocols and Models