## Slide 1
Networking Technologies
AICT012-4-2 and Version VE3
Data Link Layer and Ethernet Switching

## Slide 2: Topic & Structure of The Lesson
Topic Title | Topic Objective
Purpose of the Data Link Layer | Describe the purpose and function of the data link layer in preparing communication for transmission on specific media.
Topologies | Compare the characteristics of media access control methods on WAN and LAN topologies.
Data Link Frame | Describe the characteristics and functions of the data link frame.

## Slide 3: Topic & Structure of The Lesson (Continued…)
Topic Title | Topic Objective
Ethernet Frame | Explain how the Ethernet sublayers are related to the frame fields.
Ethernet MAC Address | Describe the Ethernet MAC address.
The MAC Address Table | Explain how a switch builds its MAC address table and forwards frames.
Switch Speeds and Forwarding Methods | Describe switch forwarding methods and port settings available on Layer 2 switch ports.
MAC and IP | Compare the roles of the MAC address and the IP address
ARP | Describe the purpose of ARP
Neighbor Discovery | Describe the operation of IPv6 neighbor discovery.

## Slide 4: Learning Outcomes
At the end of this topic, You should be able to:
  Describe the data link layer and standards
  Explain different topologies of LAN and WAN
  Compare half duplex and full duplex
  Describe access control methods
  Explain how CSMA/CD and CSMA/CA works
  Understand Data Link Frame
  Describe the Ethernet MAC address.
  Explain how a switch operates.
  Explain how a switch builds its MAC address table and forwards frames.
  Describe switch forwarding methods.
  Describe the types of port settings available for Layer 2 switches
  Compare the roles of the MAC address and the IP address.
  Describe the purpose of ARP.
  Explain how ARP requests impact network and host performance

## Slide 5: Key Terms You Must Be Able To Use
If you have mastered this topic, you should be able to use the following terms correctly in your assignments and exams:
Data Link Layer and Standards
Topologies LAN and WAN
Half and full duplex
Access Control Methods - CSMA/CD – CSMA/CA
Ethernet
MAC Address
Hexadecimal
MAC Address Table (CAM Table)
Learning / Forwarding
Filtering
Cut-Through Switching
IP address
Address Resolution Protocol (ARP)
Physical and Logical Address
ARP Broadcast
ARP Spoofing

## Slide 6: 5.1 Purpose of the Data Link Layer
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 5: Ethernet

## Slide 7: Purpose of the Data Link Layer The Data Link Layer
The Data Link layer is responsible for communications between end-device network interface cards.
It allows upper layer protocols to access the physical layer media and encapsulates Layer 3 packets (IPv4 and IPv6) into Layer 2 Frames.
It also performs error detection and rejects corrupts frames.
Notes: 6 – Data Link Layer
6.1 – Purpose of the Data Link Layer
6.1.1 – The Data Link Layer

## Slide 8: Purpose of the Data Link Layer IEEE 802 LAN/MAN Data Link Sublayers
IEEE 802 LAN/MAN standards are specific to the type of network (Ethernet, WLAN, WPAN, etc).
The Data Link Layer consists of two sublayers. Logical Link Control (LLC) and Media Access Control (MAC).
    The LLC sublayer communicates between the networking software at the upper layers and the device hardware at the lower layers.
    The MAC sublayer is responsible for data encapsulation and media access control.
Notes: 6 – Data Link Layer
6.1 – Purpose of the Data Link Layer
6.1.2 – IEEE 802 LAN/MAN Data Link Sublayers

## Slide 9: Purpose of the Data Link Layer Providing Access to Media
Packets exchanged between nodes may experience numerous data link layers and media transitions.
At each hop along the path, a router performs four basic Layer 2 functions:
  Accepts a frame from the network medium.
  De-encapsulates the frame to expose the encapsulated packet.
  Re-encapsulates the packet into a new frame.
  Forwards the new frame on the medium of the next network segment.
Notes: 6 – Data Link Layer
6.1 – Purpose of the Data Link Layer
6.1.3 – Providing Access to Media

## Slide 10: Purpose of the Data Link Layer Data Link Layer Standards
Data link layer protocols are defined by engineering organizations:
  Institute for Electrical and Electronic Engineers (IEEE).
  International Telecommunications Union (ITU).
  International Organizations for Standardization (ISO).
  American National Standards Institute (ANSI).
Notes: 6 – Data Link Layer
6.1 – Purpose of the Data Link Layer
6.1.4 – Data Link Layer Standards
6.1.5 – Check Your Understanding – Purpose of Data Link Layer

## Slide 11: Check your understanding – 5.1 Purpose of the Data Link Layer
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 12: 5.2 Topologies
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 5: Ethernet

## Slide 13: Topologies Physical and Logical Topologies
The topology of a network is the arrangement and relationship of the network devices and the interconnections between them.
There are two types of topologies used when describing networks:
  Physical topology – shows physical connections and how devices are interconnected.
  Logical topology – identifies the virtual connections between devices using device interfaces and IP addressing schemes.
Notes: 6 – Data Link Layer
6.2 – Topologies
6.2.1 – Physical and Logical Topologies

## Slide 14: Topologies WAN Topologies
There are three common physical WAN topologies:
  Point-to-point – the simplest and most common WAN topology. Consists of a permanent link between two endpoints.
  Hub and spoke – similar to a star topology where a central site interconnects branch sites through point-to-point links.
  Mesh – provides high availability but requires every end system to be connected to every other end system.
Notes: 6 – Data Link Layer
6.2 – Topologies
6.2.2 – WAN Topologies

## Slide 15: Topologies Point-to-Point WAN Topology
Physical point-to-point topologies directly connect two nodes.
The nodes may not share the media with other hosts.
Because all frames on the media can only travel to or from the two nodes, Point-to-Point WAN protocols can be very simple.
Notes: 6 – Data Link Layer
6.2 – Topologies
6.2.3– Point-to-Point WAN Topology

## Slide 16
Topologies Contention-Based Access – CSMA/CA
CSMA/CA
  Used by IEEE 802.11 WLANs.
  Operates in half-duplex mode where only one device sends or receives at a time.
  Uses a collision avoidance process to govern when a device can send and what happens if multiple devices send at the same time.
  CSMA/CA collision avoidance process:
  When transmitting, devices also include the time duration needed for the transmission.
  Other devices on the shared medium receive the time duration information and know how long the medium will be unavailable.
Notes: 6 – Data Link Layer
6.2 – Topologies
6.2.8 – Contention-Based Access – CSMA/CA
6.2.9 – Check Your Understanding - Topologies

## Slide 17: Topologies LAN Topologies
End devices on LANs are typically interconnected using a star or extended star topology. Star and extended star topologies are easy to install, very scalable and easy to troubleshoot.
Early Ethernet and Legacy Token Ring technologies provide two additional topologies:
  Bus – All end systems chained together and terminated on each end.
  Ring – Each end system is connected to its respective neighbors to form a ring.
Notes: 6 – Data Link Layer
6.2 – Topologies
6.2.4 – LAN Topologies

## Slide 18
Topologies Half and Full Duplex Communication
Half-duplex communication
  Only allows one device to send or receive at a time on a shared medium.
  Used on WLANs and legacy bus topologies with Ethernet hubs.
Full-duplex communication
  Allows both devices to simultaneously transmit and receive on a shared medium.
  Ethernet switches operate in full-duplex mode.
Notes: 6 – Data Link Layer
6.2 – Topologies
6.2.5 – Half and Full Duplex Communication

## Slide 19
Topologies Access Control Methods
Contention-based access
  All nodes operating in half-duplex, competing for use of the medium. Examples are:
    Carrier sense multiple access with collision detection (CSMA/CD) as used on legacy bus-topology Ethernet.
    Carrier sense multiple access with collision avoidance (CSMA/CA) as used on Wireless LANs.
Controlled access
  Deterministic access where each node has its own time on the medium.
  Used on legacy networks such as Token Ring and ARCNET.
Notes: 6 – Data Link Layer
6.2 – Topologies
6.2.6 – Access Control Methods

## Slide 20
Topologies Contention-Based Access – CSMA/CD
CSMA/CD
  Used by legacy Ethernet LANs.
  Operates in half-duplex mode where only one device sends or receives at a time.
  Uses a collision detection process to govern when a device can send and what happens if multiple devices send at the same time.
  CSMA/CD collision detection process:
    Devices transmitting simultaneously will result in a signal collision on the shared media.
    Devices detect the collision.
    Devices wait a random period of time and retransmit data.
Notes: 6 – Data Link Layer
6.2 – Topologies
6.2.7 – Contention-Based Access – CSMA/CD

## Slide 21: Check your understanding – 5.2 Topologies
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 22: 5.3 Data Link Frame
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 5: Ethernet

## Slide 23: Data Link Frame The Frame
Data is encapsulated by the data link layer with a header and a trailer to form a frame.
A data link frame has three parts:
  Header
  Data
  Trailer
  The fields of the header and trailer vary according to data link layer protocol.
  The amount of control information carried with in the frame varies according to access control information and logical topology.
Notes: 6 – Data Link Layer
6.3 – Data Link Frame
6.3.1 – The Frame

## Slide 24: Data Link Frame Frame Fields
Field | Description
Frame Start and Stop | Identifies beginning and end of frame
Addressing | Indicates source and destination nodes
Type | Identifies encapsulated Layer 3 protocol
Control | Identifies flow control services
Data | Contains the frame payload
Error Detection | Used for determine transmission errors
Notes: 6 – Data Link Layer
6.3 – Data Link Frame
6.3.2 – Frame Fields

## Slide 25: Data Link Frame Layer 2 Addresses
Also referred to as a physical address.
Contained in the frame header.
Used only for local delivery of a frame on the link.
Updated by each device that forwards the frame.
Notes: 6 – Data Link Layer
6.3 – Data Link Frame
6.3.3 – Layer 2 Address

## Slide 26: Data Link Frame LAN and WAN Frames
The logical topology and physical media determine the data link protocol used:
  Ethernet
  802.11 Wireless
  Point-to-Point (PPP)
  High-Level Data Link Control (HDLC)
  Frame-Relay
Each protocol performs media access control for specified logical topologies.
Notes: 6 – Data Link Layer
6.3 – Data Link Frame
6.3.4 – LAN and WAN Frames
6.3.5 – Check Your Understanding – Data Link Frame

## Slide 27: Check your understanding – 5.3 Data Link Frame
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 28: Quick Review Question
Refer to Quiz - Chapter 5 in Cisco Networking Academy platform

## Slide 29
Explain how Data Link layer support communications across data network
To compare media access control techniques and logical topologies used in networks.
Summary of Main Teaching Points

## Slide 30: Question and Answer Session
Q & A

## Slide 31: 6.1 Ethernet Frames
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 6: Ethernet

## Slide 32: Ethernet Frames Ethernet Encapsulation
Ethernet operates in the data link layer and the physical layer.
It is a family of networking technologies defined in the IEEE 802.2 and 802.3 standards.
Notes: 7 – Ethernet Switching
7.1 – Ethernet Frames
7.1.1 – Ethernet Encapsulation

## Slide 33: Ethernet Frames Data Link Sublayers
The 802 LAN/MAN standards, including Ethernet, use two separate sublayers of the data link layer to operate:
LLC Sublayer: (IEEE 802.2) Places information in the frame to identify which network layer protocol is used for the frame.
MAC Sublayer: (IEEE 802.3, 802.11, or 802.15) Responsible for data encapsulation and media access control, and provides data link layer addressing.
Notes: 7 – Ethernet Switching
7.1 – Ethernet Frames
7.1.2 - Data Link Sublayers

## Slide 34: Ethernet Frames MAC Sublayer
The MAC sublayer is responsible for data encapsulation and accessing the media.
Data Encapsulation
IEEE 802.3 data encapsulation includes the following:
Ethernet frame - This is the internal structure of the Ethernet frame.
Ethernet Addressing - The Ethernet frame includes both a source and destination MAC address to deliver the Ethernet frame from Ethernet NIC to Ethernet NIC on the same LAN.
Ethernet Error detection - The Ethernet frame includes a frame check sequence (FCS) trailer used for error detection.
Notes: 7 – Ethernet Switching
7.1 – Ethernet Frames
7.1.3 – MAC Sublayer

## Slide 35: Ethernet Frames MAC Sublayer
Media Access
The IEEE 802.3 MAC sublayer includes the specifications for different Ethernet communications standards over various types of media including copper and fiber.
Legacy Ethernet using a bus topology or hubs, is a shared, half-duplex medium. Ethernet over a half-duplex medium uses a contention-based access method, carrier sense multiple access/collision detection (CSMA/CD).
Ethernet LANs of today use switches that operate in full-duplex. Full-duplex communications with Ethernet switches do not require access control through CSMA/CD.
Notes: 7 – Ethernet Switching
7.1 – Ethernet Frames
7.1.3 – MAC Sublayer

## Slide 36: Ethernet Frames Ethernet Frame Fields
The minimum Ethernet frame size is 64 bytes and the maximum is 1518 bytes. The preamble field is not included when describing the size of the frame.
Any frame less than 64 bytes in length is considered a “collision fragment” or “runt frame” and is automatically discarded. Frames with more than 1500 bytes of data are considered “jumbo” or “baby giant frames”.
If the size of a transmitted frame is less than the minimum, or greater than the maximum, the receiving device drops the frame. Dropped frames are likely to be the result of collisions or other unwanted signals. They are considered invalid. Jumbo frames are usually supported by most Fast Ethernet and Gigabit Ethernet switches and NICs.
Notes: 7 – Ethernet Switching
7.1 – Ethernet Frames
7.1.4 – Ethernet Frame Fields
6.1.5 – Check Your Understanding – Ethernet Switching

## Slide 37: Check your understanding – 6.1 Ethernet Frames
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 38: 6.2 Ethernet MAC Address
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 7: Ethernet

## Slide 39: Ethernet MAC Addresses MAC Address and Hexadecimal
An Ethernet MAC address consists of a 48-bit binary value, expressed using 12 hexadecimal values.
Given that 8 bits (one byte) is a common binary grouping, binary 00000000 to 11111111 can be represented in hexadecimal as the range 00 to FF,
When using hexadecimal, leading zeroes are always displayed to complete the 8-bit representation. For example the binary value 0000 1010 is represented in hexadecimal as 0A.
Hexadecimal numbers are often represented by the value preceded by 0x (e.g., 0x73) to distinguish between decimal and hexadecimal values in documentation.
Hexadecimal may also be represented by a subscript 16, or the hex number followed by an H (e.g., 73H).
Notes: 7 – Ethernet Switching
7.2 – Ethernet MAC Address
7.2.1 – MAC Address and Hexadecimal

## Slide 40: Ethernet MAC Addresses 0050.0F02.352E Ethernet MAC Address
In an Ethernet LAN, every network device is connected to the same, shared media. MAC addressing provides a method for device identification at the data link layer of the OSI model.
An Ethernet MAC address is a 48-bit address expressed using 12 hexadecimal digits. Because a byte equals 8 bits, we can also say that a MAC address is 6 bytes in length.
All MAC addresses must be unique to the Ethernet device or Ethernet interface. To ensure this, all vendors that sell Ethernet devices must register with the IEEE to obtain a unique 6 hexadecimal (i.e., 24-bit or 3-byte) code called the organizationally unique identifier (OUI).
Notes: 7 – Ethernet Switching
7.2 – Ethernet MAC Address
7.2.2 – Ethernet MAC Address

## Slide 41: Ethernet MAC Addresses Ethernet MAC Address (Continued)
An Ethernet MAC address consists of a 6 hexadecimal vendor OUI code followed by a 6 hexadecimal vendor-assigned value.
Notes: 7 – Ethernet Switching
7.2 – Ethernet MAC Address
7.2.2 – Ethernet MAC Address

## Slide 42: Ethernet MAC Addresses Frame Processing
When a device is forwarding a message to an Ethernet network, the Ethernet header include a Source MAC address and a Destination MAC address.
When a NIC receives an Ethernet frame, it examines the destination MAC address to see if it matches the physical MAC address that is stored in RAM. If there is no match, the device discards the frame. If there is a match, it passes the frame up the OSI layers, where the de-encapsulation process takes place.
Notes: 7 – Ethernet Switching
7.2 – Ethernet MAC Address
7.2.3 – Frame Processing

## Slide 43: Ethernet MAC Addresses Frame Processing (Continued)
  Note: Ethernet NICs will also accept frames if the destination MAC address is a broadcast or a multicast group of which the host is a member.
Any device that is the source or destination of an Ethernet frame, will have an Ethernet NIC and therefore, a MAC address. This includes workstations, servers, printers, mobile devices, and routers.
Notes: 7 – Ethernet Switching
7.2 – Ethernet MAC Address
7.2.3 – Frame Processing

## Slide 44: Ethernet MAC Addresses Unicast MAC Address
In Ethernet, different MAC addresses are used for Layer 2 unicast, broadcast, and multicast communications.
A unicast MAC address is the unique address that is used when a frame is sent from a single transmitting device to a single destination device.
The process that a source host uses to determine the destination MAC address associated with an IPv4 address is known as Address Resolution Protocol (ARP). The process that a source host uses to determine the destination MAC address associated with an IPv6 address is known as Neighbor Discovery (ND).
Notes: 7 – Ethernet Switching
7.2 – Ethernet MAC Address
7.2.4 – Unicast MAC Address

## Slide 45: Ethernet MAC Addresses Unicast MAC Address (Continued)
Note: The source MAC address must always be a unicast.
Notes: 7 – Ethernet Switching
7.2 – Ethernet MAC Address
7.2.4 – Unicast MAC Address

## Slide 46: Ethernet MAC Addresses Broadcast MAC Address
An Ethernet broadcast frame is received and processed by every device on the Ethernet LAN. The features of an Ethernet broadcast are as follows:
It has a destination MAC address of FF-FF-FF-FF-FF-FF in hexadecimal (48 ones in binary).
It is flooded out all Ethernet switch ports except the incoming port. It is not forwarded by a router.
If the encapsulated data is an IPv4 broadcast packet, this means the packet contains a destination IPv4 address that has all ones (1s) in the host portion. This numbering in the address means that all hosts on that local network (broadcast domain) will receive and process the packet.
Notes: 7 – Ethernet Switching
7.2 – Ethernet MAC Address
7.2.5 - Broadcast MAC Address

## Slide 47: Ethernet MAC Addresses Broadcast MAC Address (Continued)
Notes: 7 – Ethernet Switching
7.2 – Ethernet MAC Address
7.2.5 - Broadcast MAC Address

## Slide 48: Ethernet MAC Addresses Multicast MAC Address
An Ethernet multicast frame is received and processed by a group of devices that belong to the same multicast group.
There is a destination MAC address of 01-00-5E when the encapsulated data is an IPv4 multicast packet and a destination MAC address of 33-33 when the encapsulated data is an IPv6 multicast packet.
There are other reserved multicast destination MAC addresses for when the encapsulated data is not IP, such as Spanning Tree Protocol (STP).
It is flooded out all Ethernet switch ports except the incoming port, unless the switch is configured for multicast snooping. It is not forwarded by a router, unless the router is configured to route multicast packets.
Notes: 7 – Ethernet Switching
7.2 – Ethernet MAC Address
7.2.6 - Multicast MAC Address

## Slide 49: Ethernet MAC Addresses Multicast MAC Address (Continued)
Because multicast addresses represent a group of addresses (sometimes called a host group), they can only be used as the destination of a packet. The source will always be a unicast address.
As with the unicast and broadcast addresses, the multicast IP address requires a corresponding multicast MAC address.
Notes: 7 – Ethernet Switching
7.2 – Ethernet MAC Address
7.2.6 - Multicast MAC Address

## Slide 50: 6.3 The MAC Address Table
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 7: Ethernet

## Slide 51: The MAC Address Table Switch Fundamentals
A Layer 2 Ethernet switch uses Layer 2 MAC addresses to make forwarding decisions. It is completely unaware of the data (protocol) being carried in the data portion of the frame, such as an IPv4 packet, an ARP message, or an IPv6 ND packet. The switch makes its forwarding decisions based solely on the Layer 2 Ethernet MAC addresses.
An Ethernet switch examines its MAC address table to make a forwarding decision for each frame, unlike legacy Ethernet hubs that repeat bits out all ports except the incoming port.
When a switch is turned on, the MAC address table is empty
Note: The MAC address table is sometimes referred to as a content addressable memory (CAM) table.
Notes: 7 – Ethernet Switching
7.3 – The MAC Address Table
7.3.1 - Switch Fundamentals

## Slide 52: The MAC Address Table Switch Learning and Forwarding
Examine the Source MAC Address (Learn)
Every frame that enters a switch is checked for new information to learn. It does this by examining the source MAC address of the frame and the port number where the frame entered the switch. If the source MAC address does not exist, it is added to the table along with the incoming port number. If the source MAC address does exist, the switch updates the refresh timer for that entry. By default, most Ethernet switches keep an entry in the table for 5 minutes.
Note: If the source MAC address does exist in the table but on a different port, the switch treats this as a new entry. The entry is replaced using the same MAC address but with the more current port number.
Notes: 7 – Ethernet Switching
7.3 – The MAC Address Table
7.3.2 - Switch Learning and Forwarding

## Slide 53: The MAC Address Table Switch Learning and Forwarding (Continued)
Find the Destination MAC Address (Forward)
If the destination MAC address is a unicast address, the switch will look for a match between the destination MAC address of the frame and an entry in its MAC address table. If the destination MAC address is in the table, it will forward the frame out the specified port. If the destination MAC address is not in the table, the switch will forward the frame out all ports except the incoming port. This is called an unknown unicast.
Note: If the destination MAC address is a broadcast or a multicast, the frame is also flooded out all ports except the incoming port.
Notes: 7 – Ethernet Switching
7.3 – The MAC Address Table
7.3.2 - Switch Learning and Forwarding

## Slide 54: The MAC Address Table Filtering Frames
As a switch receives frames from different devices, it is able to populate its MAC address table by examining the source MAC address of every frame. When the MAC address table of the switch contains the destination MAC address, it is able to filter the frame and forward out a single port.
Notes: 7 – Ethernet Switching
7.3 – The MAC Address Table
7.3.3 - Filtering Frames

## Slide 55: Video – MAC Address Tables on Connected Switches
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 56: Video – Sending the Frame to the Default Gateway
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 57: Activity – Switch it!
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 58: Activity – Switch it! - Answers
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 59: 6.4 Switch Speeds and Forwarding Methods
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 7: Ethernet

## Slide 60: Switch Speeds and Forwarding Methods Frame Forwarding Methods on Cisco Switches
Switches use one of the following forwarding methods for switching data between network ports:
Store-and-forward switching - This frame forwarding method receives the entire frame and computes the CRC. If the CRC is valid, the switch looks up the destination address, which determines the outgoing interface. Then the frame is forwarded out of the correct port.
Cut-through switching - This frame forwarding method forwards the frame before it is entirely received. At a minimum, the destination address of the frame must be read before the frame can be forwarded.
Notes: 7 – Ethernet Switching
7.4 – Switch Speeds and Forwarding Methods
7.4.1 – Frame Forwarding Methods on Cisco Switches

## Slide 61: Switch Speeds and Forwarding Methods Frame Forwarding Methods on Cisco Switches (Continued)
A big advantage of store-and-forward switching is that it determines if a frame has errors before propagating the frame. When an error is detected in a frame, the switch discards the frame. Discarding frames with errors reduces the amount of bandwidth consumed by corrupt data.
Store-and-forward switching is required for quality of service (QoS) analysis on converged networks where frame classification for traffic prioritization is necessary. For example, voice over IP (VoIP) data streams need to have priority over web-browsing traffic.
Notes: 7 – Ethernet Switching
7.4 – Switch Speeds and Forwarding Methods
7.4.1 – Frame Forwarding Methods on Cisco Switches

## Slide 62: Switch Speeds and Forwarding Methods Cut-Through Switching
In cut-through switching, the switch acts upon the data as soon as it is received, even if the transmission is not complete. The switch buffers just enough of the frame to read the destination MAC address so that it can determine to which port it should forward out the data. The switch does not perform any error checking on the frame.
There are two variants of cut-through switching:
  Fast-forward switching - Offers the lowest level of latency by immediately forwarding a packet after reading the destination address. Because fast-forward switching starts forwarding before the entire packet has been received, there may be times when packets are relayed with errors. The destination NIC discards the faulty packet upon receipt. Fast-forward switching is the typical cut-through method of switching.
  Fragment-free switching - A compromise between the high latency and high integrity of store-and-forward switching and the low latency and reduced integrity of fast-forward switching, the switch stores and performs an error check on the first 64 bytes of the frame before forwarding. Because most network errors and collisions occur during the first 64 bytes, this ensures that a collision has not occurred before forwarding the frame.
Notes: 7 – Ethernet Switching
7.4 – Switch Speeds and Forwarding Methods
7.4.2 – Cut-Through Switching

## Slide 63: Switch Speeds and Forwarding Methods Memory Buffering on Switches
An Ethernet switch may use a buffering technique to store frames before forwarding them or when the destination port is busy because of congestion.
Method | Description
Port-based memory | Frames are stored in queues that are linked to specific incoming and outgoing ports. A frame is transmitted to the outgoing port only when all the frames ahead in the queue have been successfully transmitted. It is possible for a single frame to delay the transmission of all the frames in memory because of a busy destination port. This delay occurs even if the other frames could be transmitted to open destination ports.
Shared memory | Deposits all frames into a common memory buffer shared by all switch ports and the amount of buffer memory required by a port is dynamically allocated. The frames in the buffer are dynamically linked to the destination port enabling a packet to be received on one port and then transmitted on another port, without moving it to a different queue.
Notes: 7 – Ethernet Switching
7.4 – Switch Speeds and Forwarding Methods
7.4.3 – Memory Buffering on Switches

## Slide 64: Switch Speeds and Forwarding Methods Memory Buffering on Switches (Continued)
Shared memory buffering also results in larger frames that can be transmitted with fewer dropped frames. This is important with asymmetric switching which allows for different data rates on different ports. Therefore, more bandwidth can be dedicated to certain ports (e.g., server port).
Notes: 7 – Ethernet Switching
7.4 – Switch Speeds and Forwarding Methods
7.4.3 – Memory Buffering on Switches

## Slide 65: Switch Speeds and Forwarding Methods Duplex and Speed Settings
Two of the most basic settings on a switch are the bandwidth (“speed”) and duplex settings for each individual switch port. It is critical that the duplex and bandwidth settings match between the switch port and the connected devices.
There are two types of duplex settings used for communications on an Ethernet network:
  Full-duplex - Both ends of the connection can send and receive simultaneously.
  Half-duplex - Only one end of the connection can send at a time.
Autonegotiation is an optional function found on most Ethernet switches and NICs. It enables two devices to automatically negotiate the best speed and duplex capabilities.
Note: Gigabit Ethernet ports only operate in full-duplex.
Notes: 7 – Ethernet Switching
7.4 – Switch Speeds and Forwarding Methods
7.4.4 – Duplex and Speed Settings

## Slide 66: Switch Speeds and Forwarding Methods Duplex and Speed Settings
Duplex mismatch is one of the most common causes of performance issues on 10/100 Mbps Ethernet links. It occurs when one port on the link operates at half-duplex while the other port operates at full-duplex.
This can occur when one or both ports on a link are reset, and the autonegotiation process does not result in both link partners having the same configuration.
It also can occur when users reconfigure one side of a link and forget to reconfigure the other. Both sides of a link should have autonegotiation on, or both sides should have it off. Best practice is to configure both Ethernet switch ports as full-duplex.
Notes: 7 – Ethernet Switching
7.4 – Switch Speeds and Forwarding Methods
7.4.4 – Duplex and Speed Settings

## Slide 67: Switch Speeds and Forwarding Methods Auto-MDIX
Connections between devices once required the use of either a crossover or straight-through cable. The type of cable required depended on the type of interconnecting devices.
Note: A direct connection between a router and a host requires a cross-over connection.
Most switch devices now support the automatic medium-dependent interface crossover (auto-MDIX) feature. When enabled, the switch automatically detects the type of cable attached to the port and configures the interfaces accordingly.
The auto-MDIX feature is enabled by default on switches running Cisco IOS Release 12.2(18)SE or later. However, the feature could be disabled. For this reason, you should always use the correct cable type and not rely on the auto-MDIX feature.
Auto-MDIX can be re-enabled using the mdix auto interface configuration command.
Notes: 7 – Ethernet Switching
7.4 – Switch Speeds and Forwarding Methods
7.4.5 – Auto-MDIX
7.4.6 – Check Your Understanding – Switch Speeds and Forwarding Methods

## Slide 68: Check your understanding – 6.4 Switch Speeds and Forwarding Methods
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 69: 6.5 MAC and IP
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 9: ARP

## Slide 70: MAC and IP Destination on Same Network
There are two primary addresses assigned to a device on an Ethernet LAN:
  Layer 2 physical address (the MAC address) – Used for NIC to NIC communications on the same Ethernet network.
  Layer 3 logical address (the IP address) – Used to send the packet from the source device to the destination device.
  Layer 2 addresses are used to deliver frames from one NIC to another NIC on the same network. If a destination IP address is on the same network, the destination MAC address will be that of the destination device.
Notes: 9 – Address Resolution
9.1 – MAC and IP
9.1.1 – Destination on Same Network

## Slide 71: MAC and IP Destination on Remote Network
When the destination IP address is on a remote network, the destination MAC address is that of the default gateway.
  ARP is used by IPv4 to associate the IPv4 address of a device with the MAC address of the device NIC.
  ICMPv6 is used by IPv6 to associate the IPv6 address of a device with the MAC address of the device NIC.
Notes: 9 – Address Resolution
9.1 – MAC and IP
9.1.2 – Destination on Remote Network

## Slide 72: Check your understanding – 6.5 MAC and IP
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 73: 6.6 ARP
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 9: ARP

## Slide 74: ARP ARP Overview
A device uses ARP to determine the destination MAC address of a local device when it knows its IPv4 address.
ARP provides two basic functions:
  Resolving IPv4 addresses to MAC addresses
  Maintaining an ARP table of IPv4 to MAC address mappings
Notes: 9 – Address Resolution
9.2 – ARP
9.2.1 – ARP Overview

## Slide 75: ARP ARP Functions
To send a frame, a device will search its ARP table for a destination IPv4 address and a corresponding MAC address.
  If the packet’s destination IPv4 address is on the same network, the device will search the ARP table for the destination IPv4 address.
  If the destination IPv4 address is on a different network, the device will search the ARP table for the IPv4 address of the default gateway.
  If the device locates the IPv4 address, its corresponding MAC address is used as the destination MAC address in the frame.
  If there is no ARP table entry is found, then the device sends an ARP request.
Notes: 9 – Address Resolution
9.2 – ARP
9.2.2 – ARP Functions

## Slide 76: ARP Removing Entries from an ARP Table
Entries in the ARP table are not permanent and are removed when an ARP cache timer expires after a specified period of time.
The duration of the ARP cache timer differs depending on the operating system.
ARP table entries can also be removed manually by the administrator.
Notes: 9 – Address Resolution
9.2 – ARP
9.2.6– Removing Entries from an ARP Table

## Slide 77: ARP ARP Tables on Networking Devices
The show ip arp command displays the ARP table on a Cisco router.
The arp –a command displays the ARP table on a Windows 10 PC.
R1# show ip arp
Protocol Address Age (min) Hardware Addr Type Interface
Internet 192.168.10.1 - a0e0.af0d.e140 ARPA GigabitEthernet0/0/0
C:\Users\PC> arp -a
Interface: 192.168.1.124 --- 0x10
Internet Address Physical Address Type
192.168.1.1 c8-d7-19-cc-a0-86 dynamic
192.168.1.101 08-3e-0c-f5-f7-77 dynamic
Notes: 9 – Address Resolution
9.2 – ARP
9.2.7 – ARP Tables on Networking Devices

## Slide 78: ARP ARP Issues – ARP Broadcasting and ARP Spoofing
ARP requests are received and processed by every device on the local network.
Excessive ARP broadcasts can cause some reduction in performance.
ARP replies can be spoofed by a threat actor to perform an ARP poisoning attack.
Enterprise level switches include mitigation techniques to protect against ARP attacks.
Notes: 9 – Address Resolution
9.2 – ARP
9.2.8 – ARP Issues – ARP Broadcast and ARP Spoofing

## Slide 79: Check your understanding – 6.6 ARP
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.4 – Navigate Between IOS Modes

## Slide 80: 6.7 IPv6 Neighbor Discovery (ND)
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 9: ARP

## Slide 81: IPv6 Neighbor Discovery IPv6 Neighbor Discovery Messages
IPv6 Neighbor Discovery (ND) protocol provides:
  Address resolution
  Router discovery
  Redirection services
ICMPv6 Neighbor Solicitation (NS) and Neighbor Advertisement (NA) messages are used for device-to-device messaging such as address resolution.
ICMPv6 Router Solicitation (RS) and Router Advertisement (RA) messages are used for messaging between devices and routers for router discovery.
ICMPv6 redirect messages are used by routers for better next-hop selection.
Notes: 9 – Address Resolution
9.3 – IPv6 Neighbor Discovery
9.3.2 – IPv6 Neighbor Discovery Messages

## Slide 82: IPv6 Neighbor Discovery IPv6 Neighbor Discovery – Address Resolution
IPv6 devices use ND to resolve the MAC address of a known IPv6 address.
ICMPv6 Neighbor Solicitation messages are sent using special Ethernet and IPv6 multicast addresses.
Notes: 9 – Address Resolution
9.3 – IPv6 Neighbor Discovery
9.3.3 – IPv6 Neighbor Discovery – Address Resolution

## Slide 83: Quick Review Question
Refer to Quiz - Chapter 7 and 9 in Cisco Networking Academy platform

## Slide 84
Explain the operation of Ethernet: operates in the data link layer and the physical layer. Ethernet standards define both the Layer 2 protocols and the Layer 1 technologies.
Ethernet uses the LLC and MAC sublayers of the data link layer to operate.
When a device is forwarding a message to an Ethernet network, the Ethernet header includes the source and destination MAC addresses. In Ethernet, different MAC addresses are used for Layer 2 unicast, broadcast, and multicast communications.
Explain how switch works: A Layer 2 Ethernet switch makes its forwarding decisions based solely on the Layer 2 Ethernet MAC addresses.
The switch dynamically builds the MAC address table by examining the source MAC address of the frames received on a port.
Summary of Main Teaching Points

## Slide 85
The switch forwards frames by searching for a match between the destination MAC address in the frame and an entry in the MAC address table.
Switches use one of the following forwarding methods for switching data between network ports: store-and-forward switching or cut-through switching. Two variants of cut-through switching are fast-forward and fragment-free.
Two methods of memory buffering are port-based memory and shared memory.
There are two types of duplex settings used for communications on an Ethernet network: full-duplex and half-duplex.
Summary of Main Teaching Points (Continued)

## Slide 86
Layer 2 physical addresses (i.e., Ethernet MAC addresses) are used to deliver the data link frame with the encapsulated IP packet from one NIC to another NIC on the same network.
If the destination IP address is on the same network, the destination MAC address will be that of the destination device.
When the destination IP address (IPv4 or IPv6) is on a remote network, the destination MAC address will be the address of the host default gateway (i.e., the router interface).
An IPv4 device uses ARP to determine the destination MAC address of a local device when it knows its IPv4 address.
Summary of Main Teaching Points (Continued)

## Slide 87
ARP provides two basic functions: resolving IPv4 addresses to MAC addresses and maintaining a table of IPv4 to MAC address mappings.
After the ARP reply is received, the device will add the IPv4 address and the corresponding MAC address to its ARP table.
For each device, an ARP cache timer removes ARP entries that have not been used for a specified period of time.
IPv6 does not use ARP, it uses the ND protocol to resolve MAC addresses.
An IPv6 device uses ICMPv6 Neighbor Discovery to determine the destination MAC address of a local device when it knows its IPv6 address.
Summary of Main Teaching Points (Continued)

## Slide 88: Question and Answer Session
Q & A

## Slide 89: What we will cover next
Basic Router Configurations (Network Layer)