## Slide 1
Networking Technologies
AICT012-4-2 and Version VE3
Application Layer

## Slide 2: Topic & Structure of The Lesson
Topic Title | Topic Objective
Application, Presentation, and Session | Explain how the functions of the application layer, presentation layer, and session layer work together to provide network services to end user applications.
Peer-to-Peer | Explain how end user applications operate in a peer-to-peer network.
Web and Email Protocols | Explain how web and email protocols operate.
IP Addressing Services | Explain how DNS and DHCP operate.
File Sharing Services | Explain how file transfer protocols operate.

## Slide 3: Learning Outcomes
At the end of this topic, You should be able to:
  Explain how the functions of the application layer, session layer, and presentation layer work together to provide network services to end user applications.
  Explain how common application layer protocols interact with end user applications.
  Explain how web and email protocols operate.
  Explain how the IP addressing protocols operate.
  Explain how file transfer protocols operate

## Slide 4: Key Terms You Must Be Able To Use
If you have mastered this topic, you should be able to use the following terms correctly in your assignments and exams:
HTTP
HTTPS
FTP
SMTP
POP
IMAP
DNS
DHCP

## Slide 5: 11.1 Application, Session and Presentation
Notes: Cisco Networking Academy Program
Introduction to Networks v7.0
Chapter 15: Application Layer

## Slide 6: Application, Presentation, and Session Application Layer
The upper three layers of the OSI model (application, presentation, and session) define functions of the TCP/IP application layer.
The application layer provides the interface between the applications used to communicate, and the underlying network over which messages are transmitted.
Some of the most widely known application layer protocols include HTTP, FTP, TFTP, IMAP and DNS.
Notes: 15 – Application Layer
15.1 – Application, Presentation, and Session
15.1.1 – Application Layer

## Slide 7: Application, Presentation, and Session Application Layer (Continued)
Notes: 15 – Application Layer
15.1 – Application, Presentation, and Session
15.1.1 – Application Layer

## Slide 8: Application, Presentation, and Session Presentation and Session Layer
The presentation layer has three primary functions:
    Formatting, or presenting, data at the source device into a compatible format for receipt by the destination device
    Compressing data in a way that can be decompressed by the destination device
    Encrypting data for transmission and decrypting data upon receipt
The session layer functions:
      It creates and maintains dialogs between source and destination applications.
      It handles the exchange of information to initiate dialogs, keep them active, and to restart sessions that are disrupted or idle for a long period of time.
Notes: 15 – Application Layer
15.1 – Application, Presentation, and Session
15.1.2 – Presentation and Session Layer

## Slide 9: Application, Presentation, and Session Presentation and Session Layer (Continued)
Notes: 15 – Application Layer
15.1 – Application, Presentation, and Session
15.1.2 – Presentation and Session Layer

## Slide 10: Application, Presentation, and Session TCP/IP Application Layer Protocols
The TCP/IP application protocols specify the format and control information necessary for many common internet communication functions.
Application layer protocols are used by both the source and destination devices during a communication session.
For the communications to be successful, the application layer protocols that are implemented on the source and destination host must be compatible.
Name System
DNS - Domain Name System (or Service)
TCP, UDP client 53
Translates domain names, such as cisco.com, into IP addresses.
Host Config
DHCP - Dynamic Host Configuration Protocol
UDP client 68, server 67
Dynamically assigns IP addresses to be re-used when no longer needed
Web
HTTP - Hypertext Transfer Protocol
TCP 80, 8080
A set of rules for exchanging text, graphic images, sound, video, and other multimedia files on the World Wide Web
Notes: 15 – Application Layer
15.1 – Application, Presentation, and Session
15.1.3 – TCP/IP Application Layer Protocols
15.1.4 – Check Your Understanding – Application, Session, Presentation

## Slide 11: Check your understanding – 11.1 Application, Session and Presentation

## Slide 12: 11.2 Peer to Peer
Notes: Cisco Networking Academy Program
Introduction to Networks v7.0
Chapter 15: Application Layer

## Slide 13: Peer-to-Peer Client-Server Model
Client and server processes are considered to be in the application layer.
In the client/server model, the device requesting the information is called a client and the device responding to the request is called a server.
Application layer protocols describe the format of the requests and responses between clients and servers.
Notes: 15 – Application Layer
15.2 – Peer-to-Peer
15.2.1 – Client-Server Model

## Slide 14: Peer-to-Peer Peer-to-Peer Networks
In a peer-to-peer (P2P) network, two or more computers are connected via a network and can share resources (such as printers and files) without having a dedicated server.
Every connected end device (known as a peer) can function as both a server and a client.
One computer might assume the role of server for one transaction while simultaneously serving as a client for another. The roles of client and server are set on a per request basis.
Notes: 15 – Application Layer
15.2 – Peer-to-Peer
15.2.2 – Peer-to-Peer Networks

## Slide 15: Peer-to-Peer Peer-to-Peer Applications
A P2P application allows a device to act as both a client and a server within the same communication.
Some P2P applications use a hybrid system where each peer accesses an index server to get the location of a resource stored on another peer.
Notes: 15 – Application Layer
15.2 – Peer-to-Peer
15.2.3 – Peer-to-Peer Applications

## Slide 16: Peer-to-Peer Common P2P Applications
With P2P applications, each computer in the network that is running the application can act as a client or a server for the other computers in the network that are also running the application.
Common P2P networks include the following:
    BitTorrent
    Direct Connect
    eDonkey
    Freenet
Notes: 15 – Application Layer
15.2 – Peer-to-Peer
15.2.4 – Common P2P Applications
15.2.5 – Check Your Understanding – Peer-to-Peer

## Slide 17: Check your understanding – 11.2 Peer to Peer

## Slide 18: 11.3 Web and Email Protocols
Notes: Cisco Networking Academy Program
Introduction to Networks v7.0
Chapter 15: Application Layer

## Slide 19: Web and Email Protocols Hypertext Transfer Protocol and Hypertext Markup Language
When a web address or Uniform Resource Locator (URL) is typed into a web browser, the web browser establishes a connection to the web service. The web service is running on the server that is using the HTTP protocol.
To better understand how the web browser and web server interact, examine how a web page is opened in a browser.
Step 1
The browser interprets the three parts of the URL:
http (the protocol or scheme)
www.cisco.com (the server name)
index.html (the specific filename requested)
Notes: 15 – Application Layer
15.3 – Web and Email Protocols
15.3.1 – Hypertext Transfer Protocol and Hypertext Markup Language

## Slide 20: Web and Email Protocols Hypertext Transfer Protocol and Hypertext Markup Language (Continued)
Step 2
The browser then checks with a name server to convert www.cisco.com into a numeric IP address, which it uses to connect to the server.
The client initiates an HTTP request to a server by sending a GET request to the server and asks for the index.html file.
Notes: 15 – Application Layer
15.3 – Web and Email Protocols
15.3.1 – Hypertext Transfer Protocol and Hypertext Markup Language (Cont.)

## Slide 21: Web and Email Protocols Hypertext Transfer Protocol and Hypertext Markup Language (Continued)
Step 3
In response to the request, the server sends the HTML code for this web page to the browser.
Notes: 15 – Application Layer
15.3 – Web and Email Protocols
15.3.1 – Hypertext Transfer Protocol and Hypertext Markup Language (Cont.)

## Slide 22: Web and Email Protocols Hypertext Transfer Protocol and Hypertext Markup Language (Continued)
Step 4
The browser deciphers the HTML code and formats the page for the browser window.
Notes: 15 – Application Layer
15.3 – Web and Email Protocols
15.3.1 – Hypertext Transfer Protocol and Hypertext Markup Language (Cont.)

## Slide 23: Web and Email Protocols HTTP and HTTPS
HTTP is a request/response protocol that specifies the message types used for that communication.
The three common message types are GET, POST, and PUT:
    GET - This is a client request for data. A client (web browser) sends the GET message to the web server to request HTML pages.
    POST - This uploads data files to the web server, such as form data.
    PUT - This uploads resources or content to the web server, such as an image.
Note: HTTP is not a secure protocol. For secure communications sent across the internet, HTTPS should be used.
Notes: 15 – Application Layer
15.3 – Web and Email Protocols
15.3.2 – HTTP and HTTPS

## Slide 24: Web and Email Protocols Email Protocols
Email is a store-and-forward method of sending, storing, and retrieving electronic messages across a network. Email messages are stored in databases on mail servers. Email clients communicate with mail servers to send and receive email.
The email protocols used for operation are:
    Simple Mail Transfer Protocol (SMTP) – used to send mail.
    Post Office Protocol (POP) & IMAP – used for clients to receive mail.
Notes: 15 – Application Layer
15.3 – Web and Email Protocols
15.3.3 – Email Protocols

## Slide 25: Web and Email Protocols SMTP, POP and IMAP
When a client sends email, the client SMTP process connects with a server SMTP process on well-known port 25.
After the connection is made, the client attempts to send the email to the server across the connection.
When the server receives the message, it either places the message in a local account, if the recipient is local, or forwards the message to another mail server for delivery.
The destination email server may not be online or may be busy. If so, SMTP spools messages to be sent at a later time.
Note: SMTP message formats require a message header (recipient email address & sender email address) and a message body.
Notes: 15 – Application Layer
15.3 – Web and Email Protocols
15.3.4 – SMTP, POP and IMAP

## Slide 26: Web and Email Protocols SMTP, POP and IMAP (Continued)
POP is used by an application to retrieve mail from a mail server. When mail is downloaded from the server to the client using POP the messages are then deleted on the server.
  The server starts the POP service by passively listening on TCP port 110 for client connection requests.
  When a client wants to make use of the service, it sends a request to establish a TCP connection with the server.
  When the connection is established, the POP server sends a greeting.
  The client and POP server then exchange commands and responses until the connection is closed or aborted.
Note: Since POP does not store messages, it is not recommended for small businesses that need a centralized backup solution.
Notes: 15 – Application Layer
15.3 – Web and Email Protocols
15.3.4 – SMTP, POP and IMAP (Cont.)

## Slide 27: Web and Email Protocols SMTP, POP and IMAP (Continued)
IMAP is another protocol that describes a method to retrieve email messages.
Unlike POP, when a user connects to an IMAP server, copies of the messages are downloaded to the client application. The original messages are kept on the server until manually deleted.
When a user decides to delete a message, the server synchronizes that action and deletes the message from the server.
Notes: 15 – Application Layer
15.3 – Web and Email Protocols
15.3.4 – SMTP, POP and IMAP (Cont.)
15.3.5 – Check Your Understanding – Web and Email Protocols

## Slide 28: Check your understanding – 11.3 Web and Email Protocols

## Slide 29: 11.4 IP Addressing Services
Notes: Cisco Networking Academy Program
Introduction to Networks v7.0
Chapter 15: Application Layer

## Slide 30: IP Addressing Services Domain Name Service
Domain names were created to convert the numeric IP addresses into a simple, recognizable name.
Fully-qualified domain names (FQDNs), such as http://www.cisco.com, are much easier for people to remember than 198.133.219.25.
The DNS protocol defines an automated service that matches resource names with the required numeric network address. It includes the format for queries, responses, and data.
Notes: 15 – Application Layer
15.4 – IP Addressing Services
15.4.1 – Domain Name Service

## Slide 31: IP Addressing Services DNS Message Format
The DNS server stores different types of resource records that are used to resolve names. These records contain the name, address, and type of record.
Some of these record types are as follows:
    A - An end device IPv4 address
    NS - An authoritative name server
    AAAA - An end device IPv6 address (pronounced quad-A)
    MX - A mail exchange record
When a client makes a query, the server DNS process first looks at its own records to resolve the name. If it is unable to resolve the name by using its stored records, it contacts other servers to resolve the name.
After a match is found and returned to the original requesting server, the server temporarily stores the numbered address in the event that the same name is requested again.
Notes: 15 – Application Layer
15.4 – IP Addressing Services
15.4.2 – DNS Message Format

## Slide 32: IP Addressing Services DNS Message Format (Continued)
DNS uses the same message format between servers, consisting of a question, answer, authority, and additional information for all types of client queries and server responses, error messages, and transfer of resource record information.
DNS message section | Description
Question | The question for the name server
Answer | Resource Records answering the question
Authority | Resource Records pointing toward an authority
Additional | Resource Records holding additional information
Notes: 15 – Application Layer
15.4 – IP Addressing Services
15.4.2 – DNS Message Format (Cont.)

## Slide 33: IP Addressing Services DNS Hierarchy
DNS uses a hierarchical system to create a database to provide name resolution.
Each DNS server maintains a specific database file and is only responsible for managing name-to-IP mappings for that small portion of the entire DNS structure.
When a DNS server receives a request for a name translation that is not within its DNS zone, the DNS server forwards the request to another DNS server within the proper zone for translation.
Examples of top-level domains:
    .com - a business or industry
    .org - a non-profit organization
    .au - Australia
Notes: 15 – Application Layer
15.4 – IP Addressing Services
15.4.3 – DNS Hierarchy

## Slide 34: IP Addressing Services The nslookup Command
Nslookup is a computer operating system utility that allows a user to manually query the DNS servers configured on the device to resolve a given host name.
This utility can also be used to troubleshoot name resolution issues and to verify the current status of the name servers.
When the nslookup command is issued, the default DNS server configured for your host is displayed.
The name of a host or domain can be entered at the nslookup prompt.
Notes: 15 – Application Layer
15.4 – IP Addressing Services
15.4.4 – The nslookup Command
15.4.5 – Syntax Checker – The nslookup Command

## Slide 35: Activity in Netacad – Syntax Checker – The nslookup Command

## Slide 36: IP Addressing Services Dynamic Host Configuration Protocol
Note: DHCP for IPv6 (DHCPv6) provides similar services for IPv6 clients. However, DHCPv6 does not provide a default gateway address. This can only be obtained dynamically from the Router Advertisement message of the router.
Notes: 15 – Application Layer
15.4 – IP Addressing Services
15.4.6 – Dynamic Host Configuration Protocol

## Slide 37: IP Addressing Services Dynamic Host Configuration Protocol (Continued)
The Dynamic Host Configuration Protocol (DHCP) for IPv4 service automates the assignment of IPv4 addresses, subnet masks, gateways, and other IPv4 networking parameters.
DHCP is considered dynamic addressing compared to static addressing. Static addressing is manually entering IP address information.
When a host connects to the network, the DHCP server is contacted, and an address is requested. The DHCP server chooses an address from a configured range of addresses called a pool and assigns (leases) it to the host.
Many networks use both DHCP and static addressing. DHCP is used for general purpose hosts, such as end user devices. Static addressing is used for network devices, such as gateway routers, switches, servers, and printers.
Notes: 15 – Application Layer
15.4 – IP Addressing Services
15.4.6 – Dynamic Host Configuration Protocol

## Slide 38: IP Addressing Services DHCP Operation
Note: DHCPv6 has a set of messages that is similar to those for DHCPv4. The DHCPv6 messages are SOLICIT, ADVERTISE, INFORMATION REQUEST, and REPLY.
Notes: 15 – Application Layer
15.4 – IP Addressing Services
15.4.7 – DHCP Operation

## Slide 39: IP Addressing Services DHCP Operation (Continued)
The DHCP Process:
    When an IPv4, DHCP-configured device boots up or connects to the network, the client broadcasts a DHCP discover (DHCPDISCOVER) message to identify any available DHCP servers on the network.
    A DHCP server replies with a DHCP offer (DHCPOFFER) message, which offers a lease to the client. (If a client receives more than one offer due to multiple DHCP servers on the network, it must choose one.)
    The client sends a DHCP request (DHCPREQUEST) message that identifies the explicit server and lease offer that the client is accepting.
    The server then returns a DHCP acknowledgment (DHCPACK) message that acknowledges to the client that the lease has been finalized.
    If the offer is no longer valid, then the selected server responds with a DHCP negative acknowledgment (DHCPNAK) message and the process must begin with a new DHCPDISCOVER message.
Notes: 15 – Application Layer
15.4 – IP Addressing Services
15.4.7 – DHCP Operation

## Slide 40: Check your understanding – 11.4 IP Addressing Services

## Slide 41: 11.5 File Sharing Services
Notes: Cisco Networking Academy Program
Introduction to Networks v7.0
Chapter 15: Application Layer

## Slide 42: File Sharing Services File Transfer Protocol
FTP was developed to allow for data transfers between a client and a server. An FTP client is an application which runs on a computer that is being used to push and pull data from an FTP server.
Step 1 - The client establishes the first connection to the server for control traffic using TCP port 21. The traffic consists of client commands and server replies.
Step 2 - The client establishes the second connection to the server for the actual data transfer using TCP port 20. This connection is created every time there is data to be transferred.
Step 3 - The data transfer can happen in either direction. The client can download (pull) data from the server, or the client can upload (push) data to the server.
Notes: 15 – Application Layer
15.5 – File Sharing Services
15.5.1 – File Transfer Protocol

## Slide 43: File Sharing Services Server Message Block
The Server Message Block (SMB) is a client/server, request-response file sharing protocol. Servers can make their own resources available to clients on the network.
Three functions of SMB messages:
    Start, authenticate, and terminate sessions
    Control file and printer access
    Allow an application to send or receive messages to or from another device
Unlike the file sharing supported by FTP, clients establish a long-term connection to servers. After the connection is established, the user of the client can access the resources on the server as though the resource is local to the client host.
Notes: 15 – Application Layer
15.5 – File Sharing Services
15.5.2 – Server Message Block
15.5.3 – Check Your Understanding – File Sharing Services

## Slide 44: Check your understanding – 11.5 File Sharing Services

## Slide 45: Quick Review Question
Refer to Quiz - Chapter 15 in Cisco Networking Academy platform

## Slide 46
Explain the operation of the application layer in providing support to end-user applications.
Explain how well-known TCP/IP application layer protocols and services operate.
Advantages and disadvantages of using a Peer to Peer Network.
3 common HTTP messages types.
The differences between POP3 and IMAP.
The differences between FTP and Server Message Block (SMB).
Summary of Main Teaching Points

## Slide 47: Question and Answer Session
Q & A

## Slide 48: What we will cover next
Network Security Fundamentals